# 285 nm-Laser (S-MOT)
## FLPM RMU CCT 1.1.0.0
- Laser Enable: push “on”
- Output Power: change “Power Setpoint”
  - 0.500 W for Iode spectroscopy fiber coupling
  - 2 - 2.500 W for 285 nm-SHG-Lock
- Seedpower: ~ 20 mW
Edit any other values!

## DigiLock-Module Server
1. S-MOT-Laser connected
2. start “DigiLock - SN 01265 - S-MOT-Laser”: double click of S-MOT-Laser
  1. push “Scan on”
  2. push “AutoLock”
  3. change the “Offset Value” to 0 V
  4. change the “Setpoint” (under “AutoLock”) of max slop of the middle peak
  5. Push “PID: Lock to Slop”
## Lasersystem - Typical power values
The system was build by Jan Friebe and is described in his diplomathesis.
#### 570 nm-Laser
- Outputpower after cube to 285 nm-SHG: ~ 1.2 W @ 2.5 W
- Operationpower: < @ 3 W
- Max outpupower: ??? W @ ??? W
#### Iodine spectroscopy
- For fiber: ~ 38 mW @ 0.500 W
- After fiber: ~ 29 mW @ 0.500 W (= 400 mV @ 0.500 W) [efficiency ~ 70 %]
- For fiber: ~ 220 mW @ 2.500 W
- After fiber: ~ 160 mW @ 2.500 W (= 2 V @ 2.500 W) [efficiency ~ 70 %]
### 285 nm-SHG
- Outputpower: ~ … mW @ 2.000 W
- Outputpower: ~ … mW @ 2.500 W
- Power for photodiode after SHG: ~ … mW
- Stabilized power: 80 mW
- Power for the AOM in … order: 67 mW
- Power behind the AOM: 37 mW @ 2.500 W (efficiency ~ 50 %)
Power for the Zeaman-slower: … mW
Power behind the mystical mirrow: … mW