# TiSa operation
## Optical Lattice TiSa/SHG system
1. Turn on VERDI V12 and set it to max power (~12.5 W)
2. Adjust the pump beam for the TiSa instantly after turning on the pump laser to maximize the TiSa power.
3. Wait 30 min. Realign the pump
Note: Do not forget to instantly adjust the pump after turning on the TiSa. In the worst case, you will lose lasing operation during warmup and it might be tricky to find the sweet spot again concerning power.
### Locking the TiSa
TODO
# Aligning the TiSa
Alignment for the TiSa has to be done from time to time. Some important notes:
- Be careful when taking off the cover. The alignment knobs can get stuck. If this happens, the TiSa might need to be aligned from scratch or the TiSa-Crystal can be damaged, if the pump hits it on the wrong place.
- Same is true for putting the cover back on to the TiSa. Here, make sure not to apply force. Don't make the cover fall down, since some elements can misalign pretty easily.
## Power optimization
To optimize the power, the main knobs are the Input-Mirror and the two cavity mirrors on the other side of the TiSa (one is the outcoupling mirror).
1. Optimize the pump-beam position
2. Adjust the two rear end mirrors for maximum power
3. Repeat the process
It also sometimes helps, to align the thick etalon using the knobs.
## Aligning the TiSa from scratch
DONT DO IT :D But if you have to, use the manual. Tip: If you don't have to, dont move the curved mirrors around the crystal.