## Fiber boxes 360x160
technical drawings for Inventor2018: \\afs\iqo.uni-hannover.de\user\jwolf\work\Resonator\Alugehäuse\Alugehäuse 360×160
	technical drwaing.pdf
Alu-Box	alugehaeuse_360x160.pdf
Alu-base	made to match without drawing*

### Components
#### Optics
#### Mechanics
- Alu-Box (Typ: ALS01135 - Best.Nr. M01163609)
- for thermal contact was milled of the painted surface on the inside and outside of the bottom
- Alu-base to allow to use optical components, while thermal contact is assured
- for fastening box and base are used four screw connections
#### * Annotation
- Unordered List Itemplease view the the notes on verbal agreements on the technical drawings iqo_boden_280x180.pdf!
- Die Anfertigung eines Bodens mit Schraubverbindungen an Laschen zur Nutzung der vorhandenen Bohrungen, erwies sich als zu Komplex. Die Realisierung einer 100%igen Ebenheit und somit thermischen Kontaktes der Flächen, konnte nicht gewährlistet werden. Hinzu kam die Berücksichtigung wirkender Zugkräfte, die einem thermischen Kontakt entgegengewirkt hätten. Daraufhin entschied man sich für Schraubverbindungen mittels Senkkopfschrauben im Boden der Alubox.
#### Electronics
- 6x SMA connectors for
- 1x BNC connector (Typ: 1426195 Thorlabs) for
- 4x fiber conectors (Typ: )
- 4x fiber conectors (Typ: )
## Fiber boxes 200x139
technical drawings: \\afs\iqo.uni-hannover.de\user\jwolf\work\Resonator\Alugehäuse\Alugehäuse 200×139
	technical drwaing.pdf
module	alugehaeuse_200x139_-_baugruppe.pdf
Alu-box	alugehaeuse_200x139.pdf
Alu-base	made to match without drawing*
Alu-board for AOM	iqo_aluplatte_aom_2.pdf

### Components
#### Optics
AOM (Typ: …)
#### Mechanics
- Alu-Box (Typ: ALS01115 - Best.Nr. M01142009)
- for thermal contact was milled of the painted surface on the inside and outside of the bottom
- Alu-base to allow to use optical components, while thermal contact is assured
- for fastening box and base are used four screw connections
#### Electronics
- 4x SMA connectors for
- 1x BNC (Typ: 1426195 Thorlabs) connector for
- 4x fiber connectors (Typ: ) on two opposite sides