# Multi lowpass filter
Multiple RC lowpass filters with different cutoff frequencies to switch between.
## Application
1. Vibration sensitivity measurement
2. Errorsignal for Locks

## Status
: tested and working, : minor issue/not tested, : defect
#	Status	Comment
1
2
3
4
5
6
7
8
9
10
11

## Setup

Switch: Elma 01-1104 (with gold inside), Farnell # 1876072
: cutoff frequency, : time constant, R: resistance, C: capacitance
Cutoff Frequency [Hz ]	Time Constant [ms]	Capacitance [nF]	Capacitor
4.8	33	3300	WIMA 3,3µF 50- F6
16	10	1000	WIMA MKS4 1,0µF 100-
48	3.3	330	WIMA MKC4 0.33/100-
160	1	100	µ1K100
480	0.33	33	33nK100
1600	0.1	10	10nK100

## Prototype
Multi RC lowpass filters by PTB