# Fiber Comb Control

## Installation informations
- Install first NI-drivers and LabView
- Version Fiber Comb Control: v0.4.14
- after installation put following config files in (if they were not installed automatically)…\FiberComb\etc:
  - beatcontrol
  - fibercomb - Copy.setup
  - fibercomb.setup
  - fibercomb.setup.generic-0.4.14
  - fibercomb2 -Copy.setup
  - fibercomb2.setup
- Change COM port under device manager to COM 1
## Usage informations
First start FiberLaser for better autotuning and afterwards Fiber Comb Control for controlling Repetition Rate Stepper Motor and CEO Tuner

- Start fiber comb control without and after fiber laser program!
- To optimize CEO-frequency:
  - “play” with the arrows in P-Control Laser
- To optimize a small Rep-error-signal:
  - Move in steps Forward/Backward in Repitition Rate Control
- In Lockbox Rep Rate is locked disabled (red), because it is not connected to the menlosystem electronics.

### possible errors:
- If the programm doesn´t start: Maybe COM Port wrong (should be COM1 in device manager)!
  - Start NI Device Monitor;
  - if NI card (PCI 6221) is not available: Maybe a Re-Install of NIDAQ helps (in the software/comb folder): enables PCI-6221 card