# Metamirror
## Modematching
### Parameter
Radius of curvature of mirror R1: R1= 500 mm Radius of curvature of mirror R2: R2= infinity (Incoupling side) Wavelength: λ= 1550.0 nm Length between the resonator mirrors: L= 60 mm Beam radius at cavity-waist: w0=w2 Beam radius at mirror: w1, w2 Distance between: mirror R1 and mirror R2: L mirror R2/lense 1 and lense 2: X lense 2 focal length: Z mirror R2/lense 1 and collimatorlense: Y collimatorlense and fiber: 4 mm
### Calculation
We used the programm Strahl.exe (@IQ)
#### Step 0: Choose Parameter
- Wellenlänge: 15550 nm
- Brechungsindex: 1 (Air)
Welcher Resonatortyp: linearer Resonator
#### Step 1: Beam waist calculation from resonator
- Insert
- Nr. 1: Spiegel 1 with Krümmungsradius 500mm → Brennweite: 250mm; Einfallwinkel: 0
- Nr. 2: Abstand 100 mm
- Nr. 3: Spiegel 2 with Brennweite 10000000000000 mm (so groß es ging)
  - Alternative: Planspiegel; Einfallwinkel: 0
→ Waistradius: w2= 270 µm, w1= 241.5 µm
→ FSR = 1.499 GHz
#### Step 2:
- Change with “Change” Spiegel 2 to Linse 1 - Radius Spiegel verw?=ja y
  - Brechungsindex: 1.5
  - Brennweite: -400000000000000 mm
The values of the Waistradius and Strahlradius must not change!!!

- Abstand S2 zu “Grenzfläche” Fenster
- Grenzfläche: Brechungsindex 1.5 Einfallsw=0 Radius=0 bei unendl
- Abstand dicke Fenster: 6.35mm
- Grenzfläche: Brechungsindex 0 Einfallsw=0 Radius=0 bei unendl
- Programm berechnet hieraus Strahlrad.-1ym (Nicht realistisch)
#### Step 3:
- Nr. 4: Abstand einfügen als Variable X
  - Zusammengefasst aus einzelnen Messungen: X=530mm
- Nr. 5: Linse 2 einfügen als Variable Z
  - Eingebaute Linse hat f=500mm=Z
- Nr. 6: Abstand mit festen Y und Variable X: Y - X
  - Zusammengefasst aus einzelnen Messungen: Y=1188mm
- Nr. 7: Linse 3
  - Brennweite 4 mm <fc #ff0000>(?)</fc>
- Nr. 8: Abstand 4 mm
“Zielwaist” (Strahlrad.an Faserausgang): 5.2 µm
#### Step 4: Playing with the parameters X, Y and Z for the best Überlapp
with “Variable”
Lense focal length of Lense 2 Z [mm]	500	400	300	250	200	175	150	100	50
Distance between mirror R2 and lense 2 X [mm]	576	584	589	770	894	-	-	-	-
Überlapp [%]	66.7	85.8	96.3	75.5	53.7	-	-	-	-