# Incoupling breadboard components
## Fiber collimator
Company: Schäfter+Kirchoff
- Model: 60FC-4-A2.7-45
  - Datasheet: fk60fc_e.pdf
- Housing diameter: 12mm
- Focal length: 2.75mm
- Coating: AR 1300-1750nm Coating sheet
- NA: 0.55
- Connection: FC/APC
- Schrägorientierte Koppelachse
- Integral focussing
- Amagnetic collimators made from titanium on request
- Infrared optics made of Chalcogenide glass for wavelengths > 1000 nm (see Technical Data, lens designed for λ = 2.5 μm)
- 2D-drawing: 970920020518.pdf
## Free beam optical isolator
Company: Nortus Optronic GmbH, Isowave
- Model: I-15UHP-4
- Serial Number: 45830
- Wavelength: 1515-1585nm
- Clear Aperture: 4mm
- Isolation
  - Typ: 75dB
  - Minimum: >60dB
  - testet by 1550nm: 71dB
- Transmission: 83% (90% Typ)
- Ambient Temp: 23 °C
- Insertion loss: 0.5dB
- Test report
- Datasheet
- Length: 42.3mm
- Diameter: 19mm
## DS Polaristaor
Company: Qioptiq Phtonics GmbH Link: http://photonics.specpick.com/products/polarizers/edmund-optics-inc/36-434-g335753000
- Article number: G335-753-000
  - Dimensions h=L1=L2: 10x10mm
  - Tolerance:
    - High h: -0.09mm
    - L1=L2: ±0.2mm
- Wavelength: 1100-1700nm
- Datasheet
- Special beamsplitter coatings yield highly polarized transmitted beams
- Combine extreme spectral bandwidth with superb extinction ratio and transmittance
- Extinction ratio transmission > 10,000:1 (ΦTp : ΦTs) at ± 2°
- No angular or lateral deflection of transmitted beams
- Less than λ/4 wavefront distortion at 633 nm
- Broadband coated with ARB2
- Tp > 90%
- Damage thresholds: > 2 kW/cm2 cw (488/514 nm)
- Damage thresholds: > 200 mJ/cm2 for pulses of 10 ns (1064 nm)
- Damage thresholds: > 28 mJ/cm2 for pulses of 280 fs (850 nm, 20 Hz)
## Mirror holders
Company: Thorlabs
- Typ: Polaris-K05S1 https://www.thorlabs.com/thorproduct.cfm?partnumber=POLARIS-K05S1
- 2-Adjuster Hex-Driven Design https://www.thorlabs.com/newgrouppage9.cfm?objectgroup_id=10690&pn=POLARIS-K05S1
- Designed for use with Ø1/2“ Optics
- ±5° Mechanical Angular Range
- ~11 mrad/rev Resolution
- datasheet: polaris-k05s1-specsheet.pdf
## Mirrors
Company: Thorlabs
Mirror Sepcifications
- Typ: BB0511-E04 https://www.thorlabs.com/thorproduct.cfm?partnumber=BB0511-E04
- Diameter: 12.7mm (1/2”) +0.0 mm / -0.1 mm
- Thickness: 6.0 mm (0.24“) ±0.2 mm
Coating Specifications
- Broadband Coatings: 1280-1600 nm
- Ravg > 99% for S- and P-Polarizations for Angles of Incidence from 0 to 45°
- Substrate material: Zerodur
  - Zerodur®'s coefficient of thermal expansion is 0 ± 0.100 x 10-6 /°C, which is significantly smaller than the value for fused silica, 0.55 x 10-6 /°C
- Damage Threshold: 2.5 J/cm2 (1542 nm, 10 ns, 10 Hz, Ø0.181 mm)

## Waveplate
### λ/2
Company: Crylight
- Typ: WP0210-1550 (with holder: WH1210) http://www.crylight.com/product/detail.jsp?myid=215879
- Type: Opically contacted zero Order
- Diameter: 10mm
- Outer Diameter: 12.7 mm
- Retardation: λ/2
- Wavelength: 1550nm
- Coating: AR/AR
- Size tolerance: +/-0.2
- Retardation tolerance: λ/300
- Surface Quality: 40/20
- Parallislm: <3”
- Wavefront distortion: λ/8 @ 632.8nm
- Clear aperuture: >90%
- Optical axis tolerance: +/-0.3
- Holder: WH1210
- Test Protocol: Test Protocol-Waveplates
## Waveplate Rotation Mount
Company: Thorlabs
- Typ: RSP05/M https://www.thorlabs.com/newgrouppage9.cfm?objectgroup_id=246
- Mount Ø1/2“ Optics up to 5.8 mm Thick
- Compact: 25.4 mm x 22.1 mm x 11.4 mm
- Compatible with our SM05-Threaded Lens Tubes
- One SM05RR Retaining Ring Included
- Post Mountable via 8-32 (M4) Mounting Tap
- The knurled edge of the RSP05(/M) and the 360° laser-engraved scale marked at 2° increments allow for precise
## Linear Stages
Company: Newport
- Typ: M-DS25-X https://www.newport.com/p/M-DS25-X
- Axes of Travel: X
- Maximum Stage Travel: 6.35 mm
- Load Capacity: 45 N
- Material: Aluminum
- Centered Load Capacity with BM Micrometer: 11 N
- Platform Size: 25 x 25 mm
- Sensitivity: 1 µm
## Beamsplitter Cube
Company: Thorlabs
- Typ: BS012 https://www.thorlabs.com/thorproduct.cfm?partnumber=BS012
- Size: 10.0 x 10.0 mm
- No Polarization
- Splitting: 50:50
- Wavelength: 1100 - 1600 nm