# Mode matching - plan and curve mirror
### Mirror configuration

##### Parameter
- Radius of curvature of mirror R1: R1= 1 m
- Radius of curvature of mirror R2: R2= infinity (Incoupling side)
- Wavelength: λ= 1.55×10^-6 m
- Length between the resonator mirrors: L= 485 mm
- Beam radius at waist: w0
- Beam radius at mirror: w1, w2
- Stability parameter of the resonator: g1, g2
- Distance between mirror and the waist: t1, t2
#### Beam waist calculation from resonator
Step 1: Calculate the stability parameters
Step 2: Calculate the beam waist radii on the mirrors
From thesis of Sana:
Beam Radii, 1/e^2 of the intensity
Alternative from rom Appl. Opt. 5, 1550 (1966):
In our case:
Step 3: Calculate the distance of beam waists on the mirrors and focus
Position of the beam waist on the two mirrors:
In our case: and t_2 is ≈0
Step 4: Calculate the focal length of your collimator
Take the radii on the plane w_2=w_0=496.567µm and curve mirror w_1=691.95µm and calculate the focal length f: D is the beam waist diameter of the collimated beam after the collimator and w is mode beam diameter of the fiber output. In our case is: The diameter from the light, which comes out of the fiber (1550 nm) is w= 10.5+/-0.5µm. That gives us a focal length f= 5.32044mm.
Step 4b
We did the calculation wrong. We used D=w_0 and got f=2.66022mm.