# Mode Matching - second try
### Mirror configuration
##### Parameter
- Radius of curvature of mirror R1: R1= 1 m
- Radius of curvature of mirror R2: R2= 1 m (Incoupling side)
- Wavelength: λ= 1542.0 nm
- Length between the resonator mirrors: L= 480 mm
- Beam radius at cavity-waist: w0
- Beam radius at mirror: w1, w2
- Distance between:
  - mirror R1 and mirror R2: L
  - mirror R2/lense 1 and lense 2: X
  - mirror R2/lense 1 and collimatorlense: 600mm - X
    - 615mm = optical way of the incoupling breadboard (450mm) + thickness breadboard (10mm) + distance between breadboard and vacuumchamber (30mm) + distance between vacuumchamber and cavity mirror R2 (130mm)
  - collimatorlense and fiber: 2.75 µm
We used the programm Strahl.exe (@IQ) or STRAHLFP.EXE (@PTB) (same software, but different names).
Step 1: Beam waist calculation from resonator
Step 2:
Step 3:
Step 4:
Step 4b