# Vacuum components
All CF-components are CF40!
## Vacuum pump/controller/H.V. cable
Company: Agilent Technologies
##### Pump
- Typ: VACION PLUS 40 STARCELL PUMP BASIC PUMP [Number: 9191240](http://www.agilent.com/en-us/products/vacuum-technologies/high-vacuum-pumps/ion-pumps/vacion-plus-40)
- Catalog: agilent_catalog_06_ion_section_120.pdf
- Manual: vacion_plus_40-55-75_pumps_user_manual.pdf
- Heater for Medium VIP Instructions: heater_for_medium_vip_instructions.pdf
- Auto Cad: http://www.agilent.com/cs/common/plusimages/VacIon-Plus-40-Ion-Pump-outline-drawing.png
- Other informations: “Die einzigen Einflussgrößen auf die Stabilität des Druckes sind Gaslast und Ausgasung (eigentlich auch zur Gaslast gehörend).”
##### Controller
- Typ: MINIVAC, FISCHER HV CONNECTOR, EUROPEAN PLUG 220V [Number: 9290290]
- Manual: minivac_0190_1-0290_1_1_.pdf
##### H.V. cable
- Typ: HV BAKEABLE CABLE, RADIATION RESISTANT, 13 (4 M) LONG WITH INTERLOCK FOR PUMPS CARRYING F/T [Number: 9290705]
- Length: 4m
- Datasheet/Manual: hv_radiation_resistant_cable_with_interlock-fischer_instructions.pdf
- Grtound connection notice: This pump cable can be connected to the pump only after a separate ground connection (⇐0.1Ω) is made from pump body to the ground.
## Vacuum sensor
Company: Pfeiffer Vacuum
##### Sensor
- Typ: KR 270, metallgedichtet, DN 40 CF-F (Short version)(https://www.pfeiffer-vacuum.com/de/produkte/messgeraete/activeline/activeline-transmitter/?detailPdoId=3866)
  - Manual:
    - German: ikr270_cold-cathode_german.pdf
    - English: pfeiffer_cold_cath_gage_ikr_270_english.pdf
  - Auto Cad: https://static.pfeiffer-vacuum.com/productImages/de-DE/b01cee57-690b-11e6-80ca-005056950a30.png
##### Controller
- Typ: TPG 261 (2008/12), No: PTG28030,F-No: 44308384
- Datasheet/Manual: pfeiffer_single_gauge_tpg261.pdf
##### Cable
- Typ: PT 448 250-T (https://www.pfeiffer-vacuum.com/de/produkte/messgeraete/activeline/activeline-transmitter/?detailPdoId=3381)
- Length: 3m
## Vacuum valves
### Gate valve
### Angle valve
## Other vacuum CF-components
## Vacuum isolator
Test report scan copy for vacuum compatible isolators: test_report_scan_copy_for_vacuum_compatible_isolators.pdf